Academic Msc
Dependability Modeling
- Combinatorial Models -
Erico Augusto Cavalcanti Guedes
Kádna Maria Alves Camboim
Recife, october/2010

---
Summary
1. Introduction
2. Fundamental System Reliability Models
3. Combinatorial Models

---
Summary
1. Introduction
2. Fundamental System Reliability Models
3. Combinatorial Models

---
I. Introduction
?
Reliability
Dependability
Performability
Availability

---
I. Introduction
- Dependability
  - [Laprie, 1985]
    - Computer system dependability is the quality of the delivered service such that reliance can justifiably be placed on the service
  - [Malhotra, 1994]
    - Measuse of quality, correctness, and continuity of service delivered by a system

---
I. Introduction
- Dependability
  - [IEC,2010]
  - The collective term used to describe the availability performance and its influencing factors :
    - Reliability Performance
    - Maintainability Performance
    - Maintenance Support Performance

---
I. Introduction
- Reliability:
  (Qualitative Properties)
  - Defined as the probability that a device will perform its intended functions satisfactorily for a specified period of time under specified operating conditions

---
I. Introduction
Reliability [Dhillon, 2002]

---
I. Introduction
- Reliability
  - Brief Reliability History
    - 1930s: probability concepts were applied to electric power generation-related problems
    - World War II (1939-1945): Germans used basic reliability concepts to improve reliability of their V1 and V2 missiles
    - 1950: DoD Established commitee of reliability
    - 1954: First National Symposium on Reliability and Quality Control – USA
    - 1962: a graduate degree program in reliability engineering was started by the Air Force Institute of Technology, Dayton, Ohio.

---
I. Introduction
- Reliability
  - Root Cause of Equipment Reliability Problems
    - One study based on data collected over a 30-year period categorized the root cause of equipment reliability problems into the following six groups:
Equipment Reliability Problem	%
Sales and Marketing	28
Production Scheduling	20
Maintenance	17
Production Pratices	17
Purchasing	10
Plant Engineering	8
Cloud
Computing

---
I. Introduction
Failures occur due to:
- Poor quality control
- Inadequate materials
- Incorrect use procedures
- Poor test specifications
- Over-stressed parts
- Incorrect installation or setup
- Poor manufacturing processes or tooling
- Incomplete final test
- Wrong handling or packaging
- Poor technical representative training
- Power surges
Cause for occurence of failures:
- Wear due to aging
- Inadequate or improper
preventive maintenance
- Limited-life components
- Wear due to friction
- Misalignments
- Reliability
  - Hazard (or time-dependent failure rate) of items follow a bathtub shape
Cause of failures:
- Insufficient design margins
- Incorrect use environments
- Undetectable defects
- Human error and abuse
- Unavoidable failures
There are 3 different periods:
i. Burn-in
Hazard rate decreases
ii. Useful life
Hazard rate is constant
iii. Wear-out
Hazard rate increases

---
I. Introduction
- Performability
  - [Meyer, 1980]
    - Originally, Meyer used this term mainly to reflect attributes like reliability and other associated performance attributes like availability, maintainability, etc...

---
I. Introduction
- Performability
  - [Meyer, 1980]
    - If the performance of a computing system is "degradable," performance and reliability issues must be dealt with simultaneously in the process of evaluating system effectiveness.
    - For this purpose, a unified measure, called "performability," is introduced and the foundations of performability modeling and evaluation are established.

---
I. Introduction
- Availability:
  - It is defined as the probability that the system is operating properly when it is requested for use.
  - It is defined as a fraction of time the system is providing service to its users.

---
I. Introduction
- Probability(...)
  - Commonly used lifetime distributions
    - Random Variables are used as lifetime of a device in reliability analysis
    - Feature of these random variables
      - It's continuous distributions
    - Which ones are widely used in reliability analysis?

---
I. Introduction
- Exponential
- Weibull
- Gamma
- Lognormal

---
I. Introduction
- (…) Some needed concepts:
  - Reliability Quantitative Concepts
    - The lifetime of a device can be treated as a random variable with statistical distribution and related properties(...)
    - (...)Further, the operational conditions (stress, load and/or other environmental factors)
  - Reliability function of a device[R(t)]

---
I. Introduction
- In other words:
  - R(t) is the probability that:
    - device's lifetime is larger than t;
    - device will survive beyond time t;
    - device will fail after time t
pode durar
além de...

---
I. Introduction
- Reliability Quantitative Concepts
  - Expected Value (or mean time of the lifetime T)
    - Called Mean Time To Failure(MTTF)
      (Expected Life)
Show HD
Data Sheet

---
I. Introduction
- Reliability Quantitative Concepts
  - Some more concepts...
    - For reparable devices:
      - MTTF represents the mean value to the first failure
    - After its repaired and put into operation again ...
    - … the average time to the next failure is called
      Mean Time Between Failures(MTBF)

---
I. Introduction
- Reliability Quantitative Concepts
  - The average amount of time needed to repair a failed device:
    - Mean Time To Repair (MTTR)
  - The availability, used as a measure performance, for a repairable device, can be expressed as

---
I. Introduction
- (…) Some needed concepts:
  - Probability Distribution:
    - When all possible values of a random variable are known, in conjuction with its ocurrence probabilities, we have a Probability Distribution.
    - To any set of events or propositions, there are many ways to state probabilities ...
    - … the way that one or other distribution is chose is equivalent to create different assumptions about these concerned events or propositions
P(X = x) = f(x)

---
I. Introduction
- Exponential
  - Calculate probabilities to a certain time and space among sucessive events
  - Commonly used to:
    - Arrival times
      - Queue Theory Problems
    - Fault probabilities
      - Reliability studies
  - Defined by an unique parameter
    - Mean()
      - How many events occur by unit time

---
I. Introduction
- Exponential
  - A random variable T has the exponential distribution if and only if its PDF is given by:

---
I. Introduction
- Weibull
  - Used in studies of:
    - Equipment lifetime
    - Fault estimation
  - Defined by two parameters:
    - (shape):
      - if failure rate decreases over time - (<1)
      - if failure rate is constant over time - (=1)
      - If failure rate increases over time - (>1)
    - (scale)

---
I. Introduction
- Weibull
  - PDF:

---
I. Introduction
- Lognormal
  - describes many populations that occur naturally
  - a random variable can be modeled as log-normal if it can be thought of as the multiplicative product of many small independent factors.
  - PDF:

---
Summary
1. Introduction
2. Fundamental System Reliability Models
3. Combinatorial Models

---
II. Reliability Models
- Reliability Block Diagrams (RBDs)
  - Avaliação de confiabilidade de sistemas.
  - Representam a probabilidade de sucesso de uma abordagem para modelagem de sistemas (Shooman’s).
  - É a representação gráfica de um processo ou modelo de um sistema complexo.
  - Figuras - Relações entre cada subsistema e o fluxo de informação.
    - Ex: fluxogramas

---
II. Reliability Models
- RBDs
  - Pode incluir qualquer combinação das configurações:
    - Série;
    - Paralelo simples
    - Paralelo reserva (stand-by)
    - Paralelo combinado (K-de-N)
    - Paralelo compartilhado (load-share).
  - Podemos otimizar a alocação dos diferentes componentes segundo a confiabilidade de cada um no sistema.

---
II. Reliability Models
- RBDs
  - Melhorar a Confiabilidade
    - “evitar as falhas” se obtém utilizando componentes de alta confiabilidade.
    - “tolerar as falhas” se obtém pela adição de redundâncias no sistema.
      - mais fácil para atingir uma de confiabilidade
      - nem sempre preferível,
        ● resultar em maior complexidade do sistema
        ● custos adicionais
        ● aumento tamanho

---
II. Reliability Models
- RBDs
  - Sistema com mais de uma função
  - Cada uma delas é considerada individualmente
  - Diagrama de blocos distintos
  - O desempenho do sistema depende do desempenho dos seus componentes e a importância dos componentes podem diferir

---
II. Reliability Models
- Modelos de Sistemas em Série
  - Todos os n componentes do sistema devem funcionar.
  - Se um componente falha, todo o sistema falha.

---
II. Reliability Models
- Modelos de Sistemas em Paralelo
  - Pelo menos um dos componentes é necessário para que os sistema funcione.
  - É necessário que todos os componentes falhem para que a falha do sistema ocorra.

---
II. Reliability Models
Modelos de Sistemas em Paralelo

---
II. Reliability Models
Combinações em Série-Paralelo

---
II. Reliability Models

---
II. Reliability Models
- Modelos de Sistemas em Série-Paralelo
  - Sistemas em Série-Paralelo
    - A confiabilidade de um sistema em série-paralelo é determinada a partir das confiabilidades de seus subsistemas a depender se o mesmo está em série ou paralelo.

---
II. Reliability Models
  - Sistemas em Série-Paralelo
    - Um sistema série-paralelo consiste de m módulos disjuntos que são conectados em paralelo e o módulo i para 1<= i <= m consiste de ni componentes que são conectados em series.
    - Há m caminhos mínimos e eles não têm qualquer componente em comum.

---
II. Reliability Models
  - Sistemas em Série-Paralelo

---
II. Reliability Models
- Modelos de Sistema Paralelo-Série
  - Sistema Paralelo-Série
    - Um sistema paralelo-série consiste de m módulos disjuntos que são conectados em séries e o módulo i para 1<= i <= m consiste de ni componentes que são conectados em paralelo.
    - Há m cortes mínimos e eles não têm nenhum componente em comum.

---
II. Reliability Models
- Modelos de Sistema Paralelo-Série
  - Sistema Paralelo-Série

---
II. Reliability Models
- Modelos de Sistema Standby
  - Sistema Standby
    - Outro tipo de redundância usada em engenharia de projeto é chamada redundância standby.
    - Apenas um componente está ativo no sistema.
    - Um ou mais componentes podem ser colocados no sistema, mas na condição de espera (standby).
    - Um mecanismo de comutação e detecção é usado para monitorar a operação do componente ativo.
    - Sempre que um componente ativo falha o componente em espera assume a operação.

---
II. Reliability Models
- Modelos de Sistema Standby
  - Tipos de componentes standby:
    - Hot standby: Componentes de redundância ativo.
      - Mesma taxa de falha do ativo
    - Warm standby: componentes inativos tem a taxa de falha entre 0 e a taxa de falhas do componente ativo. (cold e hot)
    - Cold standby: Taxa de falha zero.

---
II. Reliability Models
- Modelos de Sistema Standby
  - Standby

---
II. Reliability Models
- RBDs
  - Softwares para RBDs:
    - SHARPE
    - BLOCKSIM
    - ASTRO

---
II. Reliability Models
- BLOCKSIM
    - Análise da confiabilidade, mantenabilidade e disponibilidade do sistema.
    - Interface gráfica sofisticada. RBD - FTA
    - Cálculos algébricos.
    - Simulador de eventos discretos para analisar a confiabilidade, mantenabilidade, disponibilidade, capacidade máxima (throughput), custo do ciclo de vida (life cycle cost) e outras análises relacionadas.
    - Usa uma função custo padrão.

---
II. Reliability Models
- BLOCKSIM
    - Identificar componentes ou modos de falhas críticos para aumentar a performance - melhorias no projeto e planos de manutenção.
    - Reduzir riscos – vulnerabilidades.
    - Realizar a simulação de sistemas para estimar:
      - Disponibilidade média
      - Tempo médio entre falhas
      - Número de falhas esperadas
      - Custos (peça/mão-de-obra)
      - Produção
    - Técnica de programação não-linear para minimizar a função custo do sistema.

---
II. Reliability Models

---
II. Reliability Models

---
II. Reliability Models
  As distribuições de falha para todos os blocos são as seguintes:
Bloco 1: Weibull β=2.5; η=2000, γ=0
Bloco 2: Weibull β=3; η=2500, γ=0
Bloco 3: Weibull β=1.5; η=3000, γ=0
Bloco 4: Weibull β=1.9; η=5000, γ=0
Bloco 5: Exponential μ=5000, γ=0
Bloco 6: Lognormal μ=7.7142, σ=0.9653
Bloco 7: Lognormal μ=7, σ=1
Bloco 8: Weibull β=0.9; η=5000, γ=0
Bloco 9: Weibull β=5; η=6120, γ=0
Bloco 10: Weibull β=4.5; η=7000, γ=0

---
II. Reliability Models
  O BlockSim pode calcular equações muito complexas de confiabilidade segundo configurações diferentes. A equação abaixo é a equação de confiabilidade do sistema.

---
II. Reliability Models

---
II. Reliability Models

---
II. Reliability Models
Exemplo no BlockSim:
    * Server: Exponential (Mean = 45753 hr)
   * Switch: Exponential (Mean = 255,358 hr)
   * HBA: Exponential (Mean = 252,550 hr)
   * Controller: Exponential (Mean = 68,961 hr)

---
Summary
1. Introduction
2. Fundamental System Reliability Models
3. Combinatorial Models
4. Tools

---
III. Combiantorial Models
- Combinatorial Models are:
  - Non-state-space models
- They are:
    - Reliability Block Diagrams (RBD)
    - Fault Trees
    - Reliability Graphs

---
II. Combinatorial Models
- Fault Trees
  - Like RBD, Fault-Trees(FT):
    - also are Combinatorial Model Type
    - maps the operational dependency os a system on its components
  - When to use it? [FTA, 2010]
    - When the effect of a failure is known, to find how this might be caused by combinations of other failures.
    - To identify risks in a system, and consequently identify risk reduction measures.
    - to find failures which can cause the failure of all parts of a 'fault-tolerant' system.

---
II. Combinatorial Models
- Fault Trees
  - How to understand it ...
    - The failure of an item in a system is often caused by the failure of other items
  - For example:
    - a vehicle's braking failure is caused by water in the brake cylinders, which may in turn be caused by failure of the cylinder seals.

---
II. Combinatorial Models
- Fault Trees
  - Fault Tree Analysis, or FTA, provides a method of breaking down chains of failures
    (with a key addition for identifying combinations of faults that cause other faults. )
  - Combinations of faults come in two main types:
    - i. where several items must fail together to cause another item to fail (an “and” combination),
    - ii. where only one of a number of possible faults need happen to cause another item to fail (an “or'' combination).

---
II. Combinatorial Models
- Fault Trees
  - FTA diagram shows faults as a hierarchy

---
II. Combinatorial Models
- Reliability Graphs [Sahner, 1996]
  - Consists of nodes and directed graphs
  - One node is the source
    - meaning no arcs enter it
  - One node is the sink
    - meaning no arcs leave it
  - A system represented by a reliability graph fails when there is no path from the source to the sink
  - The arcs are assigned failure distributions

---
II. Combinatorial Models
- Reliability Graphs [Sahner, 1996]
  - They are equivalent to the non-series-parallel Reliability Block Diagram (RBD)
  - Failure of a component is indicated by failure of an edge
  - Each edge of the graph represents a component

---
References
[Dhillon, 2002] B. Dhillon. Engineering Maintenance: a modern approach. CRC Press, 2002.
[FTA, 2010] Fault-Tree Analysis <http://www.syque.com/quality_tools/toolbook/FTA/fta.htm>
[IEC,2010] International Electrotechnical Commission. Electropedia. Dependability Definition
<http://dom2.iec.ch/iev/iev.nsf/display?openform&ievref=191-02-03>.
[Krishna, 2008] Krishna B. Misra. Handbook of Performability Engineering, Springer, 2008.
[Kuo, 2003] W. Kuo, Ming J. Zuo. Optimal Reliability Modeling. John-Wiley and Sons, 2003.
[Laprie, 1985] J.C. Laprie. "Dependable Computing and Fault Tolerance: Concepts and
 terminology," in Proc. 15th IEEE Int. Symp. on Fault-Tolerant Computing, 1985
[Malhotra, 1994] Manish Malhotra, Kishor S. Trivedi. Power-Hierarchy of Dependability-
Model Types. IEEE Transactions on reliability, vol. 43, no. 3, 1994 september.
[Meyer, 1980] J. Meyer, On Evaluating the Performability of Degradable Computing Systems
IEEE Transactions on Computers, vol. c-29, no. 8, august 1980.
[Sahner, 1996] R. Sahner, K. S. Trivedi, A. Puliafito. Performance and reliability analysis of
computer systems: an example-based approach using the SHARPE software package.
Kluwer Academic Publishers, 1996.

---
Academic Msc
Dependability Modeling
- Combinatorial Models -
Erico Augusto Cavalcanti Guedes
Kádna Maria Alves Camboim
Recife, october/2010